## Slide 1: Vision Robotic Arm Gesture Recognition
Emanuele bianchi
Ettore candeloro
Benedetta fabrizi
Gabriele rosati

## Slide 2: The idea
Goal: use gestures and body movements to impose a motion to our robot
Two main parts:
    Vision algorithm
    Robot simulation and movement

## Slide 3: Why this project?
We wanted to combine computer vision algorithms and robotics to create a proof of concept application
Controlling remotely a robot can be useful in dangerous environments, for medical assistance and for simulation/testing

## Slide 4: Building Blocks
Block 1
Computer Vision: Hand Detector + Pose Detector
Block 2
ROS + Gazebo
First basic manipulator
Hand aperture robot control
Block 3
MoveIt
Rviz
Panda - Franka Emika
MoveIt vs Gazebo
Block 4
Direct Kinematics
Final Prototype
Block 5
Future Improvements

## Slide 5: Building Blocks
Block 1
Vision algorithm
  We used Python with the OpenCV and MediaPipe libraries.
  OpenCV allows us to work with images and video and use CV algorithms.
  Mediapipe is an ensemble of ML algorithms for different purpose developed by Google. In our case we exploit it for Hand and Pose detection. It is efficient and works also in CPU mode. This means is also employable for mobile devices.

## Slide 6: Building Blocks
Block 1
Hand Detector
  Our HandDetectorModule computes 21 hand keypoints (as shown in figure) given a webcam image.
  After the detection, custom made class methods are used to find the hand keypoints in 2D and/or in 3D and compute the hand aperture.

## Slide 7: Building Blocks
Block 1
Hand Detector Module Showcase
The HandDetector class is composed of the following methods:

## Slide 8: Building Blocks
Block 1
Computing the hand aperture
The four hand index tips are located, along the base of the hand (middle point between wrist and thumb base)
The median point between the fingers tips (thumb excluded) is computed
The L2 distance between the base of the hand point and the median fingers position is computed
The distance is then normalized by the palm size and remapped between the value 0 and 100

## Slide 9: Building Blocks
Block 1
Pose Detector
  Our PoseDetectorModule computes 33 body/pose key-points (as shown in figure) given an input image
  After the detection, various class methods are used to compute the keypoints 2D and/or 3D position and the angle between a set of 3 keypoints.
  We use those (pose) angles to modify the joint position values of our robot, so that we can control it via specific movements.

## Slide 10: Building Blocks
Block 1
Pose Detector Module Showcase
The PoseDetector class is composed of the following methods:

## Slide 11: Building Blocks
Block 1
Extracting pose angles
To extract the angles between a set of 3 keypoints (like the elbow angle given the points 12, 14, 16) we make use of the property of the scalar product between two vectors.
We create two vectors with the same origin (at the central keypoint, where we want to know the angle value)
We use the following formula to compute the angle between those two vectors:
With this method we can consider both the 2D and 3D keypoints for more robustness!

## Slide 12: Building Blocks
Block 2
Robot Environment
  Robot Operating System (ROS) is a framework for developing and programming of robots.
  It provides tipical base services of every operating system like hardware abstraction, drivers for devices, process management, etc.
  ROS is not natively real time
  Different versions exixst, we choose ROS Noetic

## Slide 13: Building Blocks
Block 2
Gazebo
  Gazebo is one of the simulation environment used with ROS
  It's fast, light and has a big community of users
  Gazebo allows Pub/Sub mechanism of ROS
  Each joint can have one or more topics and it is possible to publish on topics (e.g. modify joint values in real-time)

## Slide 14: Building Blocks
Block 2
Gazebo + ROS
  The first robot has only 2 DOF (2 rotational joints)
  The joint's values are modified with the aperture value of one human-hand provided by the Hand Detector.

## Slide 15: Building Blocks
Block 2
Gazebo + ROS Demo
  For running the simulation and script we need to launch:
    Roscore
    Gazebo world
    Robot controllers
    main.py
Notes: Roscore is a collection of nodes and programs that are pre requisite of a ros base system, you must have a roscore running in order for ros nodes to communicate

## Slide 16: Building Blocks
Block 3
MoveIt
MoveIt is an open-source robotic manipulation platform that allows to develop complex manipulation applications using ROS.
With MoveIt you can plan towards any goal position by:
  taking into account the environment scene by avoiding objects.
  interacting with the environment by grabbing objects and including them in the planning process.

## Slide 17: Building Blocks
Block 3
Rviz
Rviz (short for “ROS visualization”) is a 3D visualization software tool for robots, sensors, and algorithms.
Similar to Gazebo but have a better integration with Moveit.
At the end, we did not use MoveIt and Rviz due to performance issues on our implementation.

## Slide 18: Building Blocks
Block 3
Panda (Franka Emika)
It's an anthropomorphic manipulator with 7 DOF.
Advantages:
  It's one of the most used robot in real applications and research.
  The arm is inspired by the agility of the human arm.
  It’s completely open-source.
  (Theoretically) it’s easy to switch between the virtual simulation and the physical application.

## Slide 19: Building Blocks
Block 4
Final Prototype – Simulation/Control
We used Gazebo + ROS
We used a Direct Kinematics control with Pub/Sub mechanism
  we publish in a single Topic with the message of the following format:

## Slide 20: Building Blocks
Block 4
Final Prototype – Gestures
For moving our robot we use:
  One hand for the sixth joint
  Right-elbow angle for the fourth joint
  Left-elbow angle for the second joint
  Left-shoulder angle for the first joint
The other 3 joints are fixed

## Slide 21: Final High Level Architecture

## Slide 22: Building Blocks
Block 4
Final Prototype - Demo

## Slide 23: Building Blocks
Block 5
Future improvements
Gestures complexity and usability: Increase the set of possible gestures by adding different types of movements and improving the usability.
Test the prototype on a high-end machine, then transpose it over a real robot.
Divide each node into a standalone machine, which will be connected to the master nodes remotely.
Improve the connectivity of the solution, by exploiting camera and devices that could be connected remotely.

## Slide 24: Building Blocks
Block 5

## Slide 25: Thanks for your attention!
Emanuele Bianchi
Ettore
Candeloro
Gabriele
Rosati
Benedetta
Fabrizi
The team

## Slide 26: Backup Slides 💾

## Slide 27
Detection of Hands and Pose
Detection of Hand and Pose keypoints
If the keypoints are detected, extract the the elbow angles and hand aperture
Publish the values (adjusted) to the Panda robot

## Slide 28
Some Panda’s specs

## Slide 29
Rrbot control and pid parameters